## Slide 1
Homework 1 (Due: 17th Oct.)
(1) (a) What are the main advantage and the disadvantage of the time-frequency analysis when compared with the Fourier transform? (b) What are the main advantage and the disadvantage of the wavelet transform when compared with the short-time Fourier transform? (20 scores)
(2) Why the discrete wavelet transform is useful for (a) image compression and (b) edge detection? (10 scores)
(3) If x(t) requires N sampling points, which of the following functions require more than N sampling points? (a) x(3t), (b) x(t3), (c) x2(t), (d) exp(jt)x(t)?
Also illustrate the reasons. (10 scores)
(4) In the Hilbert-Huang transform, how do we compute the frequency without using the Fourier transform? (5 scores)

## Slide 2
(7) Write a Matlab program gwave.m that can generate a *.wav file whose instantaneous frequency is ±[a(t – b)2 + c] Hz, the length of the file is T second, and the sampling frequency is Fs Hz.
gwave (a, b, c, T, Fs)
The Matlab code should be handed out by Ceiba. (25 scores)
(6) Does satisfy the lower bound of
the uncertainty principle ( )? Why? (10 scores)
(5) (a) How does the parameter B affect the resolution of the rec-STFT?
(b) Why the Gabor transform has a better performance than the rec-STFT? (20 scores)