## Slide 1
Homework 2 (Due: 7th Nov.)
(1) Compare to the FFT-based method, what are the advantage and disadvantage of (a) the recursive method and (b) the chirp Z transform method for STFT implementation? (10 scores)
(2) Prove that (a) the Gabor transform of ( ) is . (b) The Gabor transform of 1 is .
Hint: The formulas on pages 117 and 77 may be applied. (15 scores)
(3) (a) Prove that the WDF of any signal is a real function. (b) How do we make Cohen’s class distribution for any function always be real (show the constraint for the mask function Φ(τ, η)) ? (15 scores)
(4) Which of the following signals are suitable to be analyzed by the WDF? Why? (a) exp(j3t2), (b) Music signal, (c) exp(- πt4), (d) exp(j2πt4 + j3t2)?
(10 scores)
(5) Why (a) the windowed Wigner distribution function, (b) Cohen’s class distribution, and (c) the Gabor-Wigner transform can avoid the cross term problem in some cases? (15 scores)

## Slide 2
例子：
dt=0.05;
df=0.05;
t1=[0:dt:10-dt]; t2=[10:dt:20-dt]; t3=[20:dt:30];
t=[0:dt:30];
f=[-5:df:5];
x=[cos(2*pi*t1),cos(6*pi*t2),cos(4*pi*t3)];
B=1;
tic
y=recSTFT(x,t,f,B);
toc
(i) 程式碼要由 ceiba 繳交
(ii) 用 function 的指令寫成函式，
(iii) 自己選一個 input x, 用你們的程式將 output y 算出來並畫出來
(iv) 用 tic 和 toc 的指令來計算程式的 running time
(v) 不可以用 direct implementation 的方法
(6) Write a program for the rectangular short time Fourier transform .
y = recSTFT(x, t, f, B) (35 scores)
x: input, t: samples on t-axis, f: samples on f-axis,
[-B, B]: interval of integration, y: output