## Slide 1
Homework 4 (Due: 26th Dec.)
(1) Illustrate the following terms. (a) color noise; (b) scaling function (about the wavelet transform); (c) scalogram. (15 scores)
(2) What are the vanish moments of
(a)
(b) x(t) = 2 for -1 < t < 1, x(t) = -1 for 1 < |t| < 3, x(t) = 0 otherwise.
(10 scores)
(3) (a) What is the most important advantage of the Haar transform nowadays?
(b) How many entries of the 2k-point Haar transform are equal to 0, 1, and -1? Express the solutions in term of k. (15 scores)
(4) Among the STFT, the WDF, and the Hilbert-Huang transform, which one is better for the applications of (a) tone analysis, (b) random process analysis, (c) multiplexing, and (d) analyzing the variation of temperature?
Also illustrate the reasons. (15 scores)

## Slide 2
(7) Write a Matlab program of the Hilbert-Huang transform.
y = hht(x, t, thr)
x: input, y: output (each row of y is one of the IMFs of x), t: samples on the t-axis, thr : the threshold used in Step 7.
In Step 8, the number of non-boundary extremes can be no more than 3.
The Matlab code should be handed out by Ceiba. (30 scores)
Example: t = [0: 0.01: 10];
x = 0.2*t + cos(2*pi*t) + 0.4*cos(10*pi*t);
thr = 0.2;
y = hht(x, t, thr);
(5) Which of the following signal is not an IMF? Why?
(a) sin(t) + t, (b) cos(t3). (5 scores)
(6) Write two concepts you learned from the oral presentation on 12/5.
(10 scores)